## Slide 1: Department of Mechanical and Aerospace Engineering
High Powered Rocketry Club
2015-2016 CDR Presentation
Notes: UPDATED

## Slide 2: CDR Overview
Subscale test flight
Launch vehicle
  Subsystems design
  Recovery
  Performance
AGSE
  Design
  Subsystems execution
  Power supply
Conclusions
Notes: UPDATED

## Slide 3: Subscale Test Flight Vehicle
Diameter: 4 inches
Length: 72.25 inches
Weight: 10.15 lbs
Static Margin: 2.33 caliber
Recovery: 48 inch main
18 inch drogue
Motor: AeroTech I284W-10
Notes: UPDATED

## Slide 4: Subscale Test Flight Vehicle - Simulations
Length: 72.25 inches
Diameter: 4 inches
Weight: 10.15 lbs
Motor: AeroTech I284W-10
Apogee: 1798 ft
Maximum Velocity: 361 ft/s
Time to Apogee: 10.7 seconds
Total Flight Time: 66.8 seconds
Notes: UPDATED

## Slide 5: Subscale Test Flight
Date: 11/28/2015
Apogee: 1033 ft in 10 seconds
Max Velocity: 245 ft/s
Total Flight Time: 46 seconds
Notes: UPDATED

## Slide 6: Vehicle Design - Layout
Component | Dimension
Overall Vehicle Length | 102 in
Diameter | 5.5 in
Notes: Need comparable picture

## Slide 7: Vehicle Design - Nosecone
Element | Dimension
Maximum Diameter | 5.5 in
Exposed Length | 18.5 in
Shoulder Length | 5.0 in
Notes: UPDATED

## Slide 8: Vehicle Design - Airframe
5.5” diameter fiberglass
Body tube separated into three main sections
Payload compartment in upper airframe section
Notes: UPDATED

## Slide 9: Vehicle Design – Fin Section
Notes: UPDATED

## Slide 10: Vehicle Design – Airbrakes
Notes: UPDATED

## Slide 11: Vehicle Design – Motor Selection
AeroTech L1150R
Weight: 4.19 lbs
Length: 20.87 in
Diameter: 2.95 in
Average thrust: 258.5 lbs
Total impulse: 790.6 lb-s
Burn time: 3.1 s
Thrust-to-weight ratio: 8.816:1
Notes: UPDATED

## Slide 12: Vehicle Design - Stability
CG 64.3” nose ref.
CP 76.3” nose ref.
Static Margin 2.18
63 feet per second as the forward rail button leaves the launch rail
Notes: UPDATED

## Slide 13: Vehicle Design - Weight
Component | Weight (lbs)
Fiberglass | 9.10
Nosecone | 1.79
Centering Rings | 0.25
Bulkheads | 2.43
Fins | 0.98
Motor Housing | 0.46
Motor | 8.10
U-bolts | 1.25
Parachutes | 0.59
Shock Cord / Recovery Hardware | 0.59
Avionics Hardware | 1.00
Airbrake | 1.00
Payload | 0.44
Total | 27.98
Notes: UPDATED

## Slide 14: Vehicle Recovery - Parachutes
18 inch drogue parachute
1.1 ounce Ripstop, 400 pound Sprectra Lines shroud lines with a 3/8 inch nylon bridle attached to a 600 pound swivel
48 inch main parachute
1.1 ounce Ripstop, 400 pound braided nylon shroud lines with a ½ inch nylon bridle attached to a 1500 pound swivel
60 inch main parachute
Standard nylon toroidal, 400 pound flat nylon shroud lines with a 5/8 inch nylon bridle attached to a 1500 pound swivel

## Slide 15: Vehicle Recovery - ARRD
ARRD is a black powder activated release device
Separates drogue parachute shock cord from sample section
Necessary for mission requirements
Experiment performed to determine appropriate charge size
  Complete release of eye-bolt on all tests
  Successful at 0.1 grams black powder
Notes: UNCHANGED

## Slide 16: Vehicle Recovery - Avionics
Two avionics compartments:
  One Stratologger SL100 altimeter, one Strattologger CF altimeter, and two Entacore AIM 3.0 altimeters powered with four 9V batteries
  Two sleds, and two GPS boards
  Upper avionics: ARRD at 1100 ft, nosecone from forward airframe at 1000 ft AGL
  Lower avionics: Drogue charge at apogee, aft airframe and fin section at 700 ft AGL

## Slide 17: Vehicle Recovery - Forward Avionics
Notes: UPDATED

## Slide 18: Vehicle Recovery - Aft Avionics
Notes: UPDATED

## Slide 19: Vehicle Recovery– Event Sequence
Apogee
18” Drogue Parachute
Notes: UPDATED

## Slide 20: Vehicle Recovery– Event Sequence
1000 ft AGL
48” Main Parachute
Notes: UPDATED

## Slide 21: Vehicle Recovery– Event Sequence
700 ft AGL
60” Main Parachute
Notes: UPDATED

## Slide 22: Mission Performance – Kinetic Energy
Main Nosecone Kinetic Energy
Main Fin Section Kinetic Energy
Vehicle under Drogue Velocity
Notes: UPDATED

## Slide 23: Vehicle Recovery - Wind Drift
Wind (mph) | Forward Airframe (ft) | Fin Section (ft)
0 (blue) | 0 | 0
5 (green) | 404 | 396
10 (brown) | 807 | 792
15 (yellow) | 1211 | 1188
20 (red) | 1614 | 1584
Notes: UPDATED

## Slide 24: Vehicle Performance– Flight Profile
Open rocket simulation using AeroTech L1150
Notes: UPDATED

## Slide 25: Vehicle Performance - Fluent CFD
Notes: UPDATED

## Slide 26: Vehicle Performance - Fluent CFD
Notes: UPDATED

## Slide 27: AGSE - Design
Notes: UPDATED

## Slide 28: AGSE - Design
Notes: UPDATED

## Slide 29: AGSE - Design
Notes: UPDATED

## Slide 30: AGSE - Design
Notes: UPDATED

## Slide 31: AGSE - Progression
Grab the Sample
Insert Sample into Mold
Raise the Rocket
Insert the Igniter
System Ready to Launch
Start System
Notes: UNCHANGED

## Slide 32: Interfaces
Kill and pause switches on AGSE
Indicator LED
Altimeter switches
BeagleBone board
Notes: UNCHANGED

## Slide 33: Robotic Arm
6 degrees of freedom
2:1 gear ratio
180 degrees of rotation at each joint
Able to lift ~1 lb at 24 in
Uses 4.8 - 6 V power supply and up to 10 A current draw
Notes: UPDATED

## Slide 34: Robotic Arm
Notes: UPDATED

## Slide 35: Gripper
Provides 2 additional degrees of freedom
180 degrees rotation around wrist
Able to open 1.3 in
Uses 6 V power supply
Notes: UNCHANGED

## Slide 36: Model of Arm
MATLAB used to plot arm at different servo angles
Code calculates angles in real time
Notes: UNCHANGED

## Slide 37: Raising the Rocket
Sector Gear
  8 in radius
  Mounted to the side of launch rail
Drive Gear
  1 in radius
  Keyway for connection to motor
Planetary Gearbox Stepper Motor
  NEMA 23 frame size
  Max holding torque: 29.5 ft-lb
  Required holding torque: 19.5 ft-lb
  Leadshine M542 stepper driver
Notes: UPDATED

## Slide 38: Launch Rail Raising Experiment
Setup:
  12 inch radius pulley
  19.5 lb weight hanging radially
  Simulated 19.5 ft-lb required holding torque
Results:
  Successfully verified stepper motor capabilities
Function Generator Square Wave Frequency (Hz) | 90 Degree Rotation Time (s) | Calculated Launch Rail Rise Time (s)
700 | 6.67 | 58.48
1000 | 4.31 | 32.56
1500 | 2.82 | 21.31
1750 | 2.41 | 18.21
1900 | 2.05 | 15.49
2000 | N/A | N/A
Notes: UPDATED

## Slide 39: Igniter Insertion
NEMA 17 Stepper Motor
ST-6128 Stepper Driver
Design Concept:
Stepper motor rotates threaded rod
Threaded Delrin square plate moves vertically due to side plates
Igniter on dowel moves upward into rocket motor
Experiment
Successful verification of igniter insertion speed
21 inch translation in less than 45 seconds
Notes: UPDATED

## Slide 40: AGSE Electrical Schematic
Notes: UPDATED

## Slide 41: Power Supply
37 V System
11.1 V System
Notes: UNCHANGED

## Slide 42: 37 V System
Used to power two stepper motors
  Raising rocket
  Inserting igniter
Stepper motors require high voltage to meet torque requirements to raise the rocket
37 V System
Notes: UNCHANGED

## Slide 43: 11.1 V System
11.1 V System
Systems on this battery
  BeagleBone Black
  Robotic arm servos
  Robotic arm controller
Step-Down voltage regulators to convert to the desired voltage of different electronics
Notes: UNCHANGED

## Slide 44: Conclusions
  Developed subsonic, reusable launch vehicle to deliver a payload to 5280 feet AGL with a safe return.
  Created an airbrake system to accurately achieve the target apogee altitude.
  Created a replacement servo adapter to fit in place of the larger, old robotic arm servos.
  Developed a fully autonomous AGSE to capture the payload, insert it into the vehicle, erect the vehicle, and insert the igniter.

## Slide 45
Questions?
Notes: UNCHANGED