## Slide 1: Department of Mechanical and Aerospace Engineering
High Powered Rocketry Club
2015-2016 PDR Presentation

## Slide 2: PDR Overview
  Vehicle
    Design
    Recovery
    Mission Performance
    Interfaces and Integration
  AGSE
    Design
    Arm
    Rocket Erection
    Igniter Insertion
  Budget
  Safety
  Subscale
  Questions

## Slide 3: Vehicle Design - Nosecone
Ogive shaped nosecone for higher subsonic drag
Element | Dimension
Maximum Diameter | 5.5 in
Exposed Length | 16 in
Shoulder Length | 5.0 in

## Slide 4: Vehicle Design - Airframe
5.5” diameter fiberglass tube
Body tube separated into four compartments sealed by bulkheads
Payload receptacle on forward airframe section

## Slide 5: Rocket Layout
Airbrakes
Payload Bay
1.5' Parachute
4' Parachute
6' Parachute
Telemetry/Airbrake Control

## Slide 6: Airframe – Payload Zone

## Slide 7: Vehicle Design - Avionics
Two avionics compartments
Primary and redundant altimeters
  Forward: Entacore AIM 3.0
  Aft: Statologger CF and SL100
9V batteries, 3D printed sled, GPS
Upper avionics: drogue charge 5280’, ARRD 1100’, nosecone from upper airframe 1000’
Aft sled middle and fin section 700’

## Slide 8: Forward Avionics

## Slide 9: Aft Avionics

## Slide 10: Vehicle Design – Fin Section
0.75” bulkhead will be epoxied 3” from the upper surface of the airframe
Centering rings on either side of fin tabs
Element | Dimension
Length | 34.5 in
Diameter | 5.5
Element | Dimension
Width | 0.25 in
Height | 4.75in
Root chord | 12 in
Tip chord | 4.25 in

## Slide 11: Vehicle Design – Airbrakes
Dual airbrake system
Airbrakes deployed with linear actuator
Deploy at 3000-4000 feet
Bring apogee to desirable level

## Slide 12: Vehicle Design - Stability
CG 63.0” nose ref.
CP 75.5” nose ref.
Static Margin 2.09
54 ft/s as the uppermost rail button leaves the launch rail
Center of Gravity
Center of Pressure

## Slide 13: Vehicle Design - Motor
AeroTech L1150R
  20.87” Length
  0.295” Diameter
  258.5 lbf*s Impulse
  3.1 second Burn Time 1.68 lbs
  4.19 lb Propellant Mass
  Stability Margin increases from 2.093.21

## Slide 14: Thrust Curve

## Slide 15: Vehicle Recovery
Apogee

## Slide 16: Vehicle Recovery: ARRD
ARRD uses black powder release
Separates drogue chute shock cord from upper airframe

## Slide 17: Vehicle Recovery
1000 ft

## Slide 18: Vehicle Recovery
700 ft

## Slide 19: Wind Drift
Wind (mph) | Forward Airframe(ft) | Fin Section (ft)
0 | 0 | 0
5 | 404 | 396
10 | 807 | 792
15 | 1211 | 1188
20 | 1614 | 1584

## Slide 20: Mission Performance – Flight Profile
Open rocket simulation using AeroTech L1150R

## Slide 21: Mission Performance – Velocity

## Slide 22: Mission Performance – Kinetic Energy

## Slide 23: AGSE Design

## Slide 24: AGSE Design

## Slide 25: AGSE Design

## Slide 26: AGSE Design

## Slide 27: AGSE Progression
Grab the Sample
Insert Sample in Foam
Raise the Rocket
Insert the Igniter
System Ready to Launch
Start System

## Slide 28: Robotic Arm
4 Degrees of Freedom
5:1 Gear Ratio
180 degrees of rotation at each joint
Able to lift ~1 lb at 24”
6V draw and current up to 10 A

## Slide 29: Gripper
Provides 2 additional DOF
180 degrees rotation around wrist
Able to open 1.3”
6V draw

## Slide 30: Model of Arm
MATLAB used to plot arm at different servo angles

## Slide 31: Reachable Points
MATLAB plot of all points the arm is able to reach in 3 dimensional space

## Slide 32
Progression of the system will be time based, with each subsystem set to begin operating after a set period of time from the start
AGSE Progression

## Slide 33: Raising the Rocket
Planetary Gearbox Stepper Motor
  Max Holding Torque: 29.5 ft-lb
  Step Angle: 0.039 deg
  ~22,000 steps for 85 deg launch rail rotation
Sector Gear
  Gear Ratio: 7.5:1
Required holding torque:
  18.69 ft-lb

## Slide 34: Igniter Insertion
Linear Actuator System
NEMA 17 Stepper Motor
Design Concept:
Stepper motor rotates threaded rod.
Threaded hexagonal plate moves vertically due to side plates.
Igniter on dowel moves upward into rocket motor.

## Slide 35
Electrical Schematic
Overview

## Slide 36: Battery Systems
37 V System
11.1 V System

## Slide 37: 37 V System
Used to power two stepper motors
  Raising Rocket
  Raising Igniter
Stepper motors require high power to meet torque requirements to raise the rocket
37 V System

## Slide 38: 11.1 V System
11.1 V System
Step-Down voltage regulators to convert to the desired voltage of different electronics
Systems on this battery
  BeagleBone Black
  Robotic arm
  Robotic arm controller
  Rocket Stepper Motor Driver
  Igniter Stepper Motor Driver

## Slide 39: Subscale Demonstrator
Subscale is 70% of fullscale
Aerotech I284W Motor
Dual Deploy
18 in. Drogue
48 in. Parachute

## Slide 40: Subscale Motor Thrust Curve
Aerotech I284W

## Slide 41: Community Outreach
Tripoli Summer Low-Mid Power Launches
STEM Career Fair for Students with Disabilities
Thales Academy Rocket Unit Kick-Off
YMCA Kite and Rocket Day
Sigma Gamma Tau Boy Scout Merit Badge Event

## Slide 42: Thank You
QUESTIONS?